## Slide 1: NanoFluids

## Slide 2: What are Nanofluids?
Nanofluids is Colloids = Base fluids + Nanomaterials
Nanomaterials (e.g. nanoparticles, nanofibers, nanotubes, nanowires, nanorods, nanosheet, or droplets)
These particles, generally stable metals or metal oxide:
  Al2O3
  ZrO2
  SiO2
  Fe3O4
  Cu
  Au
  Carbon
  Diamond
  Fullerene
  Polymer (Teflon), etc.

## Slide 3: Preparation of Nanofluids
One-step method
(Production of nanoparticle and dispersion in a base fluid are done simultaneously)
  Direct evaporation technique
  Chemical reduction
  Laser ablation
  Microwave Irradiation
  Phase-Transfer Method
Two-step method
(The nanomaterials are first produced then dispersed into a fluid)

## Slide 4: Characterization of nanoﬂuids
Nanoﬂuids are characterized by the following techniques: SEM, TEM, XRD, FT-IR, DLS, TGA and zeta potential analysis.
Important analysis for nanofluids:
  DLS analysis: estimate the average disperse size of nanoparticles in the base liquid media and
  TGA : study the influence of heating and melting on the thermal stabilities of nanoparticles.
  Zeta potential value is related to the stability of nanoparticle dispersion in base ﬂuid.

## Slide 5: Properties of nanofluids
Thermal conductivity
Viscosity
Convective heat transfer
Density
Speciﬁc Heat

## Slide 6: Thermal conductivity
K of nanofluids depends on many parameters;
base fluids, volume fraction, particle size, shape, temperature, surface charge, pH value, Brownian motion of nanoparticles, effect of clustering, nanolayer, dispersion techniques.
The experimental data shows that k of nanofluid do not agree with the theoretical models results.
Transient hot wire technique not transient wire

## Slide 7: Viscosity
Viscosity is a measure of the tendency of a liquid to resist flow.
The viscosity of nanofluid depends on many parameters;
base ﬂuid properties, particle volume fraction, particle size, particle shape, temperature, pH value, surfactants, dispersion techniques, particle size distribution, particle aggregation and temperature.
linear relationship between viscosity and volume concentration .

## Slide 8: Application of nanoﬂuids
Automobile applications
Solar energy applications
Mechanical applications
Reactor-heat exchange
Optical application
Biomedical applications
Electronics cooling

## Slide 9: Challenges of nanofluids
The main issues and challenges of nanofluids are;
The disagreement between most of experimental data with the theoretical model predictions
The poor characterization of the Nano suspensions.
The lack of understanding of the complex physical phenomena responsible for the anomalous behavior of nanoﬂuids

## Slide 10: Conclusion
Thermal conductivity, viscosity and speciﬁc heat models of nanoﬂuids are many in literatures.
The requirement to improve the efficiency of thermal systems relies highly on the enhancement of thermal conductivity of base ﬂuid
The experimental work on viscosity, speciﬁc heat and pressure drop of nanofluid and their dependence on temperature are limited

## Slide 11: Conclusion
Stability of nanoﬂuids is one of the key challenges hindering the widespread practical application of nanoﬂuids.
Studies showed that stability depend on pH, sonication time, different types of shapes and sizes of nanoparticles with different base ﬂuids, nanoﬂuid preparation methods, volume fraction and surfactants.